## Slide 1
Jacob Friedberg
1
MyCobots 320pi and Custom Ros2 Msgs.

## Slide 2: Outline:
2
What is the MyCobot
Control Interfaces
  Forward and Inverse Kinematics
  Python, C++, ROS, RVIZ
  PymyCobot.
How to work with the robot
  Connecting.
  Programming.
The project.
  Project description.
  Tips for the project
Custom Ros2 Messages
  Interface Available
  Coding example
Short Assignment

## Slide 3: What is mycobot

## Slide 4: What is mycobot
6 DOF(Degrees of freedom) arm
  1kg payload capacity.
  350mm Working radius
  24v IO
  Servo motors with encoders.
  E-stop capable
Raspberry pi4 B as the brain.
  ESP32 to run encoders
  ATOM in the EOAT
320PI2_650x.png (650×650) (shopify.com)

## Slide 5: Control Interfaces

## Slide 6: Control Interfaces
Two kinematic methods
  Forward and Inverse (Mycobot can do both)
Forward kinematics
  From the base of the chain forward to the end effector.
  Set each joint individually by providing a list of angles
  All joints forward of a change in angle are altered.
    Change joint 2 and joint 3-5 move, but joint 1 does not.
IK-1.png (486×513) (alanzucconi.com)

## Slide 7: Control Interfaces
Inverse Kinematics
  Reverse of forward kinematics
  Choose a position in x,y,z space for the end effector, and solve for the joints to get there
Inverse kinematic solvers.
  Many different types
    Analytical (exact solution)
    Numerical (Approximation based)
      Optimization based SGD
  Warning: STOCHASTIC
320PI2_650x.png (650×650) (shopify.com)

## Slide 8: Control Interfaces

## Slide 9: Control Interfaces
Programming interfaces
  Python
    PymyCobot
  C++(May not be supported on our model)
  C#
  Java Script
  Blockly(Scratch programming)
Additional programming support
  ROS
  ROS2
  RVIZ
320PI2_650x.png (650×650) (shopify.com)

## Slide 10: Control Interfaces

## Slide 11: Control Interfaces
PymyCobot
  Python Library Github
  Our main tool for programming the robot.
  Provides: 2 Introduction to API · GitBook (elephantrobotics.com)
    Forward and Inverse kinematic control
    Status functions
    Gripper control
    Direct Servo Control and encoder control
ROS2 Implementation on myCobot
  Super minimal.
  Examples, just wrap pymycobot functions in a ros2 subscriber node.

## Slide 12: How to work with the robot

## Slide 13: How to work with the robot
Connecting
  A PDF instruction for all operating systems should have been passed around via email(Thanks Kristie)
  Short version
    The Scooby class robots have been named based on the sticker on them. We have Velma and Shaggy.
    Connect to the AirVandalRobotMoscow network
    Using a remote desktop connection program(Microsoft or equivalent) provide the host name(Name of robot, shaggy or velma) and provide “er” as the username.
    Use the password REDACTED to login

## Slide 14: How to work with the robot
Programming the Robot.
  The process for programming the Robot with ROS2 is straightforward but crude.
  Since there are no action clients/servers we have to make our own.
    You could implement your own action servers(ROS2 Action Server) or make a very basic version using publishers and subscribers.
    You will create some nodes(likely subscribers) on the MyCobot to receive a message/goal(start some action perhaps?) and perform an action using the pymycobot API.
    Publish a message to indicate you are done.
  Connect everything up on your laptop using RCLPY similar to the create3 projects. Sequence everything in one place.

## Slide 15: The Project

## Slide 16: The Project
The Goal
  You will have 3 robots in total. 1 create3 and 2 elephant robot arms
  Start with the create3 near one of the arms. You will need to have one of the arms pick up an object and place it on top of the create 3.
  Have the create 3 drive to the other arm across the room. This can be a straight line if you so choose.
    You are allowed to use multiple docking stations to give you points of reference in the path.
  Stop the create3 Infront of the other arm.
  Have the arm unload the create 3.

## Slide 17: The Project
Tips
  First thing to do: Define how you are going to synchronize actions between the robots.
    In my mind this can be done by sending custom messages to the robot on a specific topic to indicate state.
    Smart sequencer that orchestrates all movement.
  You can work on each part individually and integrate at the end but don’t wait too long. Unexpected issues happen.
  You need to build the supporting RCLPY functions on the MyCobots to use in your Project program.

## Slide 18: Custom Ros2 Messages

## Slide 19: Custom Ros2 Messages
ROS2 Messages
  A way to send data between Robots and ROS2 Nodes. We used the hazard vector which is a message for the Create 3.
  Subset of types available.

## Slide 20: Custom Ros2 Messages
CODING EXAMPLE
Creating custom msg and srv files — ROS 2 Documentation: Humble documentation

## Slide 21: Short Assignment

## Slide 22: Short Assignment
Connect to the robot and make it move in any way.
  Show me you are ready to program the project.
  Turn in a video or show me in person.
  Submit 1 per group(3 total submissions)